## Slide 1: Heat Stress in Construction
Chesapeake Region Safety Council Annual Conference XXV, April 8, 2014
Michele M. Twilley, DrPH, CIH
President, Aria Environmental Inc.
Gavin H. West, MPH
Research Analyst, CPWR
Notes: Image: Ironworker using a thermic lance and a supplied air respirator.
http://www.elcosh.org/image/235/i001144/1144.html
Credit: Mount Sinai/CHEP

## Slide 2: Acknowledgements
Dr. Bruce Lippy, CPWR
Dr. Laura Welch, CPWR
Dr. Rosemary Sokas, Georgetown University
Bernard Mizula, Mizula LLC
Notes: I’d like to acknowledge Bruce Lippy, Laura Welch, and Rosemary Sokas for lending me their expertise while I prepared this presentation.
In particular, I’d like to thank to Bernie Mizula for allowing me to borrow certain content from his heat stress training materials.
These slides will be made available at a later date, and we will have time for questions at the end of the presentation.

## Slide 3: By the end of this presentation you will be able to:
Provide a few facts and figures illustrating the burden of occupational heat stress
Explain five reasons why non-fatal heat-related illnesses are still a major concern
Describe several personal, medical, and work-related risk factors for heat-related illness in construction
Use the hierarchy of controls to implement effective heat stress solutions
Access additional resources for effective heat stress management

## Slide 4: Heat is the leading cause of weather-related deaths in the US
Photo by FEMA/Greg Henshall
U.S. Air Force photo by Edward Aspera Jr.
Photo by FEMA/Greg Henshall
Photo by Justin Hobson via Wikimedia Commons
Photo by NASA via Wikimedia Commons
Notes: National Weather Service statistical data show that heat causes more fatalities per year than floods, lightning, tornadoes, and hurricanes combined (NOAA 2011).
National Oceanic and Atmospheric Administration (NOAA) (2011) National Weather Service. Heat: a major killer. Available at: http://www.crh.noaa.gov/lmk/?n=noaaexcessiveheat Accessed: 17 March 2014
New Hartford, Iowa, June 9, 2008 -- Heavy rains flooded this small town of 698 last night. The fire chief's high-suspension jeep is being used to shuttle residents to their homes so they can check damage and rescue their pets. Photo by Greg Henshall / FEMA - Location: New Hartford, IA
Lightning over Las Cruces, New Mexico
Source: United States Air Force, VIRIN 040304-F-0000S-002 (and VIRIN 060822-F-1111A-001)
Author: U.S. Air Force photo by Edward Aspera Jr.
Category F5 tornado (upgraded from initial estimate of F4) viewed from the southeast as it approached Elie, Manitoba on Friday, June 22nd, 2007.
Source: Transferred from en.wikipedia; transferred to Commons by User:Gump Stump using CommonsHelper.
Author: Justin Hobson (Justin1569 at en.wikipedia)
Before the year 2004, only two tropical cyclones had ever been noted in the South Atlantic Basin, and no hurricane. However, a circulation center well off the coast of southern Brazil developed tropical cyclone characteristics and continued to intensify as it moved westward. The system developed an eye and apparently reached hurricane strength on Friday, March 26, before eventually making landfall late on Saturday, March 27, 2004. The crew of the International Space Station was notified of the cyclone and acquired excellent photographs of the storm just as it made landfall on the southern Brazilian state of Santa Catarina (the storm has been unofficially dubbed “Cyclone Catarina”). Note the clockwise circulation of Southern Hemisphere cyclones, the well-defined banding features, and the eyewall of at least a Category 1 system. The coastline is visible under the clouds in the upper left corner of the image.
Source: NASA
Author: Astronaut photograph ISS008-E-19646 was taken March 7, 2004, with a Kodak DCS760 digital camera equipped with an 50-mm lens, and is provided by the Earth Observations Laboratory, Johnson Space Center.

## Slide 5: Occupational heat fatalities, USA 2003-2008
Notes: This infographic represents 196 American workers who died on the job due to heat exposure between 2003-2008.
Each icon represents a real person.
Construction workers are shown in blue, and all other occupations are represented by the orange figures.
Dividing the number of deaths shown here by the number of days in this six year time period shows that a worker died of heat exposure every 11 days on average.
Every 11 days seems to be a frequent loss of life, but this oversimplified statistic doesn’t even account for non-workdays and the fact that most of these deaths occurred during warmer months.
This information from the US Census of Fatal Occupational Injuries shows that the highest proportion of these deaths (36%) were in the construction industry (Jackson & Rosenberg, 2010).

## Slide 6: Aside from being primarily construction workers, what else can we say about these 196 workers who suffered heat-related fatalities?

## Slide 7: They were overwhelmingly male…
Chart: 
| Male | Female
Gender | 191 | 5
(Jackson & Rosenberg, 2010)
Notes: Larry Jackson of NIOSH and Howard Rosenberg of UC Berkeley took a closer look at the CFOI records and found that these 196 workers who died from exposure to environmental heat were mostly male (97%, 191).

## Slide 8: Younger than you might expect…
Chart: 
(Jackson & Rosenberg, 2010)
Chart: Age in years
| <55 | 55+
Age in years | 145 | 51
Notes: They were also younger than you might expect.
Some were less than 20 years old, while others were 65 and older.
The median age of the group was in the range of 35-44 years.
At least 74% of those who died were younger than 55.
During heat waves, it’s not uncommon to hear of elderly citizens succumbing to heat-related illnesses in their homes.
It’s important to note however that in occupational settings younger workers often fall victim to excessive heat exposure as well.

## Slide 9: And mostly white
Chart: 
(Jackson & Rosenberg, 2010)
Chart: Race/Ethnicity
| white-non-Hispanic | Hispanic | black-non-Hispanic | not available
Race/Ethnicity | 95 | 63 | 31 | 7
Notes: Nearly half of the 196 were white-non-Hispanic workers (48%, N=95), at least 32% were Hispanic (N≥63), and 16% were black-non-Hispanic (N=31).
To recap, workers who died of heat exposure in the US between 2003-2008 were predominantly male, mostly white, and usually less than 55 years old.

## Slide 10: We’ve covered who and how many have died on the job due to heat exposure, but what about where?

## Slide 11: OSHA’s heat fatality map, 2008-2013
https://www.osha.gov/SLTC/heatillness/map.html
Notes: Moving forward, let’s take a look at heat-related deaths on the job over the next six year span, starting in 2008.
This map created by OSHA includes only outdoor workers and does not include all worker fatalities from heat exposure during this time period.
Even so, the map helps illustrate the serious issue of workers dying on the job due to heat stress.
It also gives us an idea of where these deaths are occurring.
From OSHA website:
“This map shows locations of outdoor worker, heat-related fatalities between 2008 and 2013. It is not an exhaustive list of all worker fatalities from heat exposure during this time period. It includes only those fatalities that involve workers who are covered by either the Federal Occupational Safety and Health Administration (Federal OSHA) or a State OSHA plan. Some fatalities reported to the Bureau of Labor Statistics (BLS) are outside Federal and State plan OSHA jurisdiction and are not included. In addition, reporting and update timeframes for the Federal OSHA information systems used to generate this map vary from BLS and are based on the circumstances of the case, which may result in inconsistencies.
The map provides a geographic reminder that Water.Rest.Shade are vital to providing a safe and healthful environment when working outdoors in the heat. For each fatality, basic information about the type of workplace, work task, and work conditions is provided if available. This information was drawn from both preliminary and final investigation reports. Links to available inspection data are provided for incidents recorded on OSHA’s Statistics & Data webpage. Once an OSHA investigation is complete, any preliminary data will be updated. Additional incidents will be added as information becomes available.”

## Slide 12: OSHA’s heat fatality map, 2008-2013
https://www.osha.gov/SLTC/heatillness/map.html
Notes: The map shows a large swath of real estate in the western and central regions of the country [callout] with few or no heat-related occupational fatalities in recent years.
Conversely, the map also shows high numbers of fatalities in states such as California [callout] and Texas [callout].
A number of factors influence the geographic distribution of heat-related morbidity and mortality; such as type of industry, size of the workforce, and differences in reporting, but we’d certainly expect climate variation to be a significant factor.

## Slide 13
(Hyatt et al., 2011)
Notes: These maps are from a study by Hyatt, Lemke and Kjellstrom entitled Regional maps of occupational heat exposure: past, present, and potential future.
I cropped the original image and stretched it out a bit to hopefully make it easier for you folks to see. As a result, data from 1975 are not shown, and the maps may be slightly distorted.
The maps show wet bulb globe temperatures or WBGTs indoors and outside in the shade during the hottest part of the day for Central America and the southern US.
From left to right, the maps show temperatures during June, July, and August, respectively.
The maps across the top were constructed using actual data from the year 2000.
The bottom three maps show WBGTs for a climate change model predicting an increase of 3 degrees Celsius after the year 2000.
Moving from green to red, we see an increased risk of heat-related illness, which I will also refer to as HRI, with red regions indicating extreme risk of HRI.
Once again, these are WBGTs indoors and in the shade, not in direct sunlight!
Notice that the large swath of real estate I pointed out on the last slide roughly corresponds with the greener portions of the 2000 maps.
Logically, regions where more occupational heat-related deaths occurred tend to correspond with higher WBGT areas.
In this particular climate change model, we see much less green and the emergence of extreme risk areas indicated by red on the lower three maps.
If this particular climate change model proves accurate, US workers in the future may be subjected to extreme risk of heat-related illness even while working in the shade.
The takeaway message here is that climate change could make occupational heat exposure an increasingly serious problem moving forward.
Fig. 4. WBGT (indoors and outside in the shade during the hottest part of the day) for Central America and the southern US in 1975, 2000, and a scenario where WBGT is increased by 3 degrees Celsius from the year 2000.

## Slide 14: Despite cooler climates, outdoor workers still die of heat exposure in northern states
https://www.osha.gov/SLTC/heatillness/map.html
Notes: Despite cooler climates, outdoor workers still die of heat exposure in northern states such as Minnesota, Washington, Wisconsin, and Massachusetts.
OSHA’s map is interactive.
Clicking an icon close to our current location opens a pop-up box, describing the death of a heavy and civil engineering construction worker who died in the summer of 2012 in Washington DC.
The summary states that the employee was outside doing paving work when he collapsed and eventually died of hyperthermia. It was 98 degrees F that day with a heat index of 102 degrees.

## Slide 15: Heat Stress can be like a volcano - explosive and deadly
Slide content courtesy: Bernard Mizula
Notes: Heat stroke, a medical emergency which Michele will discuss in more detail, can come on suddenly and explosively.
Without swift intervention, heat stroke can easily lead to permanent brain damage or death.
We’ve talked about the burden of heat-related fatalities, but there are many more cases of heat-related illnesses than heat stroke. They represent a larger portion of the volcano.
An even greater portion of the volcano is filled with jobs that involve excess heat.
Any incident should be given serious consideration as it could erupt into heat stroke.
Many jobs expose workers to excess heat, and it is important to recognize that all of them could lead to illness and stroke if preventive measures are not taken consistently.

## Slide 16: “The incidence of occupational heat-related disorders in the US is not known although millions of workers have some level of exposure to hot environments.” Gubernot DM, Anderson GB, Hunting KL (2013) The epidemiology of occupational heat exposure in the United States: a review of the literature and assessment of research needs in a changing climate. Int J Biometeorol.
Notes: Better estimates are available for heat-related fatalities, but a recent epidemiological review published in December of 2013 concluded that:
“The incidence of occupational heat-related disorders in the US is not known although millions of workers have some level of exposure to hot environments.”

## Slide 17: The US Military collects some of the best data on work-related HRIs
Photo by FEMA/Mike Moore
Notes: St. Paul, Minn., April 1, 2009 -- Members of the Armed Forces and FEMA during a daily briefing in the Emergency Operations Center in St. Paul. Planning the response to any disaster takes teamwork and open communications; this meeting is in response to flooding along the Red River in western Minnesota. Mike Moore/FEMA - Location: St. Paul, MN

## Slide 18
(Armed Forces Health Surveillance Center, 2011)
a Rate per 1,000 person-years
311
2,576
Notes: This is part of a table taken from a US Armed Forces Medical Surveillance report documenting HRIs in 2010.
Like the volcano, we see a smaller number of heat stroke cases [callout] and a much larger number of HRIs [callout].
In 2010, there were 311 cases of heat stroke and 2,576 cases of other heat injuries in the US Armed Forces active component.
Thus for each case of heat stroke there were more than 8 cases of other heat related illnesses.
Also note that workers less than 30 years old [callout] accounted for the majority of cases and experienced the highest rates of HRIs [callout].
The rates shown in this table are expressed per 1,000 person-years.
Table 1. Incident cases and incidence ratesa of heat injury, active component, U.S. Armed Forces, 2010 (a Rate per 1,000 person-years)
In the U.S. Military Health System, the most serious of heat-related injuries are considered notifiable medical events. Since 31 July 2009, a notifiable case of “heat stroke” (ICD-9-CM: 992.0) has been defined as a “severe heat stress injury, specifically including injury to the central nervous system, characterized by central nervous system dysfunction and often accompanied by heat injury to other organs and tissue.” Notifiable cases of heat injuries other than heat stroke (“unspecified effects of heat” [ICD-9-CM: 992.9]) include “moderate to severe heat injuries associated with strenuous exercise and environmental heat stress” … “that require medical intervention or result in lost duty time.” All heat injuries that require medical intervention or result in lost duty are reportable. Cases of “heat exhaustion” (ICD-9-CM: 992.3-992.5) that do not require medical intervention or result in lost duty time are not reportable.

## Slide 19: More accurate estimates of construction HRIs are available for some states

## Slide 20: Several industries stood out for rates of HRI (WA state comp data, 1995-2005)
Chart: 
| Highway, Bridge and Street Construction | Roofing Construction | Fire Protection
NAICS industries with the highest workers’ compensation HRI average annual claims incidence rate (WA state, 1995-2005) | 44.8 | 59 | 80.8
Incidence rates per 100,000 FTE from Bonauto et al. (2007)
Notes: Although Washington isn’t the hottest state, their workers’ comp records are easily accessed and widely used by researchers.
Bonauto et al. (2007) analyzed workers’ comp claims for HRI in WA state from 1995-2005.
The highest average annual incidence rates of HRI by industry (NAICS) are shown in this chart I created using their data.
The rates shown are per 100,000 Full-Time-Equivalents or FTEs.
Aside from fire protection, the industries with the highest rates of HRI were highway, bridge and street construction along with roofing construction.
Site preparation construction and poured concrete foundation and structural construction were next on the list with a rate of 35.9
When the authors looked at occupational classification (2000 SOC) instead of industry, they found that construction laborers accounted for the highest proportion (8.5%) of all work-related HRIs analyzed during the eleven year period.
These data are useful for identifying construction trades or occupations that may experience high risk or prevalence of HRIs.
**
FTE = Full Time Equivalents.
NAICS = North American Industry Classification System

## Slide 21: So there are lots of non-fatal HRIs, but what’s the big concern?
Potential for heat stroke
Related health effects
Decreased productivity
Increased risk of injury
Synergism
Notes: I mentioned earlier that heat-related illness can quickly erupt into heat stroke, which often leads to death or permanent brain damage, but there are additional concerns.
Occupational heat exposure has been associated with chronic health effects, productivity losses, and acute accidents and injury.
There are also potential synergistic effects to consider.

## Slide 22: Workers exposed to heat may be at increased risk for:
Death from ischemic heart disease (Wild et al., 1995)
Compromised blood pressure control (Ganio et al. 2012; Crandall et al. 2010)
Kidney disease, particularly stones (Tawatsupa et al., 2012; Atan et al., 2005; Borghi et al., 1993)
Notes: Ischemic Heart Disease is also known as Coronary Artery Disease - a common disease that can cause heart attacks.
It is also common knowledge that exposure to the sun’s UV rays can increase one’s risk of skin cancer.

## Slide 23: Staying hydrated can help avoid having to pass one of these through your system
Image by Wilfredor via Wikimedia Commons
Notes: Image description: Kidney Stone of Rafael Urdaneta General in Rafael Urdaneta Museum Interior

## Slide 24: NASA study, A Compendium of Human Responses to the Aerospace Environment found that as temperatures rise, work quality suffers
NASA CR-1205-1 |  |  |  |  |  |  | 
Temperature (oF) | 75 | 80 | 85 | 90 | 95 | 100 | 105
% Loss in work output | 3 | 8 | 18 | 29 | 45 | 62 | 79
% Loss in accuracy |  | 5 | 40 | 300 | 700 |  | 
Slide content courtesy of: Bernard Mizula
Notes: Here are some striking data from a study by NASA showing that work quality decreases when temperature increases.
We see loss of both accuracy and work output starting at 80 degrees F.
At 95 degrees F, there was a 45% loss in work output and a 700% loss in accuracy.
I confess that I’ve not read this study in detail and am not aware of what type of work was performed, but there are a number of studies showing heat-associated losses in productivity across a variety of working conditions.
This relationship was described as far back as 1974 in a paper by Axelsson entitled “Influence of heat exposure on productivity”.

## Slide 25: Heat exposure increases risk of accidents and injuries
Image by OSHA Training Institute,
Southwest Education Center
As a side note, can you spot the bad work
practices shown here?
Image by OSHA Training Institute, Southwest Education Center
Notes: You wouldn’t want to faint due to heat syncope while working on a roof or a ladder.
As a side note, can you spot the bad work practices shown in these images?
Summary Statement: Ladder not tied off to prevent sideways movement. Ladder less than 3 ft above roof access point. No fall protection, there should be a fall protection system in place, such as a fall restraint system to prevent workers from falling to a lower level. Worker does not have PPE, workers should be supplied proper PPE such as eye protection, gloves, harnesses, etc.
Tags: Falls, Roofer/Waterproofer, Residential, Images
Credit: OSHA Training Institute, Southwest Education Center
elcosh image ID: i000893

## Slide 26: Synergism – heat may magnify chemical exposures and vice versa
Notes: Pharmacological studies have shown an increase in the absorption and effects of certain drugs when they are administered simultaneously to heat exposure (Sidhu et al., 2011; Vanakoski & Seppala, 1998)
Furthermore, epidemiological studies on the impact of simultaneous exposure to heat stress and air pollution revealed a significant effect on mortality rate (Katsouyanni et al., 1993; Rainham & Smoyer-Tomic, 2003).
Extrapolating these findings to the workplace gives reason to believe that concomitant exposure to heat stress and chemicals is likely to increase the potential risk for workers’ health (Bourbonnais et al., 2013).
This is relevant to construction industry, where workers are often exposed to vapors, dusts, gases, and fumes.

## Slide 27
“Awareness of the medical conditions, medications or
personal risk factors that place an individual at risk for HRI
should be a required component of a training program.” (Bonauto et al., 2007)

## Slide 28: Personal risk factors for HRI
Low physical fitness (Epstein, 1990)
Obesity (Maeda et al., 2006)
Clothing, PPE
Age > 65
Acclimatization
Image By Fj.toloza992 , via Wikimedia Commons
Notes: Many factors influence one’s sensitivity to heat.
Personal risk factors include low levels of physical fitness and obesity.
Clothing choice matters. NIOSH recommends light-colored, loose-fitting, breathable clothing such as cotton. Non-breathing synthetic clothing is not advised.
As Michele will discuss, PPE can have a strong effect on the body’s ability to cool itself.
Being over 65 years old is commonly cited as a risk factor for HRI.
The older you are the more likely you are to have chronic diseases that may interfere with your body’s ability to thermoregulate.
Workers over 65 should be made aware this fact.
I do have two concerns I’d like to mention at this point.
My own personal belief is that sometimes there’s a fine line between using health status as a means of protecting workers versus a means of discrimination.
Second, I caution you to be wary of mixed messages. It can be dangerous for workers who don’t fit these risk categories to believe that they are immune to heat stress.
Anyone can fall victim to heat stress given the right conditions.
Recall my previous slide showing that 74% of US workers who died of heat exposure between 2003-2008 were less than 55 years old.
The military surveillance data we reviewed also showed the highest rates of HRI among workers in their 20’s.
Granted, younger workers in the military are more likely to be on active duty as opposed to having a desk job, which may have influenced these rates.
I don’t have additional hard evidence to discuss regarding risk of HRI among young employees, but I can share my own experience.
During my 20’s, I was young, strong, and healthy.
At the peak of physical fitness, I was prone to feeling somewhat invincible, and it was difficult to imagine falling victim to illness or injury, such as HRI.
Pushing beyond your limits as a young worker eager to prove yourself is admirable in some respects but can result in a bad outcome.
Young workers are often new workers, meaning that they might not yet be acclimated to the heat.
Without proper training, a young and inexperienced worker may also fail to recognize the importance of acclimatization.
Acclimatization is critical for preventing HRI!

## Slide 29: HRIs happen early on the job among new workers
Cal/OSHA investigated HRI cases from 2005
  46% on day 1
  80% on days 1-4
https://www.osha.gov/SLTC/heatillness/heat_index/pdfs/all_in_one.pdf
Notes: Cal/OSHA investigated cases of heat related illness that occurred in 2005.
In almost half of the incidents, the worker involved was on their first day of work.
In 80% of cases, the worker had been on the job for 4 days or less.
These numbers underscore the importance of acclimating workers to the heat.

## Slide 30: NIOSH suggests limiting heat exposures during acclimatization
Day Number | Experienced Heat Worker | New Worker
1 | 50% | 20%
2 | 60% | 40%
3 | 80% | 60%
4 | 100% | 80%
5 | 100% | 100%
Slide courtesy of: Bernard Mizula
(NIOSH, 1986)
Notes: Michele will cover these guidelines in more detail, but for now just notice the difference in recommended maximum heat exposures for new workers vs. experienced heat workers.
From NIOSH document Criteria for a Recommended Standard: Occupational Exposure to Hot Environments Revised Criteria 1986:
“Gradually increase exposure time in hot environmental conditions over a 7-14 day period.
For new workers, the schedule should be no more than 20% exposure on day 1 and a no more than 20% increase on each additional day.
For workers who have had previous experience with the job, the acclimatization regimen should be no more than a 50% exposure. on day 1, 60% on day 2, 80% on day 3, and 100% on day 4.”

## Slide 31: Medical risk factors for HRI
Diabetes (Yardley et al., 2013)
Heart and lung diseases (Becker et al. 2011)
Sickle cell trait (Becker et al., 2011)
Fever (Grogan & Hopkins, 2002)
Skin diseases (Grogan & Hopkins, 2002)
Prior heat stroke (Epstein, 1990)
Drugs, alcohol
Meds
Notes: Medical risk factors for HRI include diabetes, heart and lung disease, sickle cell, fever, and skin disease.
Special attention should be paid to workers with previous heat stroke since it might reflect an underlying cause for heat susceptibility.
Drugs, alcohol, and certain medications can also increase risk of HRI.

## Slide 32
(Becker et al., 2011)
Notes: Here is list of medications and substances that contribute to HRI.
Medical confidentiality is important to consider in this context, but this information can at least be provided to workers to help them better understand their personal susceptibility to heat stress.
This table mostly shows medications but also includes drugs of abuse; such as cocaine, alcohol, and laxatives.
Coffee is a common diuretic that can contribute to HRI via dehydration.

## Slide 33: Work-related factors in construction also increase risk of HRIs
Tools and machinery
Elevated surfaces
Heavy workloads
Simple accommodations
Temporary employment
Direct sunlight
PPE requirements
(Xiang et al., 2013)

## Slide 34: Constant use of machinery and power tools can generate radiant heat
Image by:
Mount Sinai/
CHEP
Notes: Image credit: Mount Sinai/ CHEP
eLCOSH image ID: i001408

## Slide 35: Working on elevated or reflective surfaces can make the sun’s rays even more intense
Image by: Bruce Lippy
Notes: I should also point out that these workers are using a dangerous scaffold without fall protection, putting them at risk of serious injury.
Summary: This photo of elevated work taking place near Cancun, Mexico shows workers without fall protection on a dangerous scaffold at great risk of falling.
Image Credit: Bruce Lippy
eLCOSH ID: i002614

## Slide 36: Heavy workloads can increase core temps and cause electrolyte imbalance and dehydration through sweat loss
Image by: Cement Masons/Washington State
Department of Labor and Industries
Notes: This image shows workers hand screeding cement with a 2x4, which is not an easy task.
Summary Statement:
Hand screeding to level out concrete creates a lot of stress on the wrist, hands and back. Try screeding with one foot in front of the other to reduce bank bending and excessive reaching. Concrete workers should use proper work precautions against contact dermatitis and skin sensitization. For additional information refer to either to the ELCOSH library or the Laborers Health and Safety Fund's reference material on working safely with cement.
Image Credit: Cement Masons/Washington State Department of Labor and Industries
eLCOSH ID: i001174

## Slide 37: Simple accommodations don’t guarantee easy access to water, shade, or cooled spaces
Image credit: Kiewit
Power Constructors
Notes: Image credit: Kiewit Power Constructors
eLCOSH image id: i002612

## Slide 38: Temporary employment is common in construction and can complicate training and prevention efforts
Image by: OSHA Training Institute,
Southwest Education Center
Notes: For example , a temporary employer might not be aware of a worker’s acclimatization status.
Summary Statement: All workers on site should be using proper PPE. Workers and supervisors should attempt to keep site clear of clutter. Electrical cords should be kept away from physical damage.
Image credit: OSHA Training Institute, Southwest Education Center
eLCOSH image id: i000710

## Slide 39: Many trades are often exposed to direct sunlight
Image by: Mount Sinai/ CHEP
Notes: This is a bit of a no-brainer, but many trades are often exposed to direct sunlight.
Credit: Mount Sinai/ CHEP
ID: i001414

## Slide 40: Last but not least… PPE can be a major risk factor for HRI
Image by: Mount Sinai/CHEP
Notes: The workers shown here are wearing level C protective clothing.
At this point, I’d like to hand over the reigns to Michele.
Summary Statement: Level C protective clothing. 1/2 face APRs with 100 series combination OVA filters.
Credit: Mount Sinai/CHEP
ID: i000629

## Slide 41: Physiology of Heat Stress, Heat Strain and Heat Related Injury
Michele M. Twilley, DrPH, CIH
Aria Environmental, Inc.
Notes: Good afternoon! I would like to thank Gavin West with CPWR for sharing with us the magnitude and severity of heat related illness as both a public and occupational health problem. I am going to speak to you about the biological and physiological aspects of heat stress, strain and illness.

## Slide 42: Physiology
Homeostasis
38°C
37°C
36°C
http://www.freefitnessguru.com/blog/bodybuilding-2/lower-core-temperature-for-30-performance-gain/.php
http://www.pricefalls.com/product/Beistle-53055-TEM-90-in.-x-37-in.-Moveable-Thermometer-Stand-Out/1678740?utm_source=ShareASale&utm_medium=cpa&utm_term=&utm_content=&utm_cam&s0=3vy4aacl
https://sites.google.com/site/bentleysbiology/ib/option-e/e-5-the-human-brain
Notes: Everyone’s core temperature cycles around a slightly different genetically determined version of 37°C set by the hypothalamus. Our bodies are constantly producing heat as the natural byproduct of metabolism. That heat is continuously lost to the environment.
Homeostasis exists when the quantity of heat produced is equal to the amount lost. If heat production and heat loss are not in balance, body temperature will rise or fall according to the stress experienced. Heat stress occurs when the body temperature extends above and beyond this narrow range.

## Slide 43: Heat Loss by Vasodilation
Radiation, conduction and convection from the skin.
http://y13hb.files.wordpress.com/2013/03/vasoconstriction.png
Notes: Overheating of the hypothalamic thermostat increases the pace of heat loss through vasodilation which sends heated blood to the skin’s surface where heat can be dissipated through radiation, conduction and convection. Approximately 65% of the heat loss is through vasodilation.
The image on the left shows the dilation of the blood vessels that are closer to the skin’s surface. Heat loss through vasodilation works best when the surrounding temperature is lower than body temperature. By contrast, the image on the right hand side of the screen shows vasoconstriction near the skin surface to prevent heat loss.
http://y13hb.files.wordpress.com/2013/03/vasoconstriction.png

## Slide 44: Heat Loss by Sweating
Notes: Approximately 30% of the body’s heat loss is through evaporative cooling of sweat. The human body has 2 to 4 million sweat glands and a maximum capacity to produce 1 to 2 liters of sweat per hour. Cooling the body through this mechanism requires dry air. Humid air or humid air trapped in protective clothing doesn’t allow for effective evaporation of perspiration. Just remember the old phrase, “Its not the heat, it’s the humidity.”
A third mechanism is behavioral. We seek cooler conditions for our bodies by seeking shade, removing clothing and avoiding heat altogether.
http://www.medterms.com/script/main/art.asp?articlekey=8017

## Slide 45: Physiology of Heat Stress
During both rest and activity the human body tries to maintain a core temperature of 37°C
CORE TEMP
BLOOD VOL
Normal
http://www.behance.net/gallery/Active-Microclimate-Cooling-System/4833917
Normal
Notes: During both rest and activity the human body tries to maintain a core temperature of 37°C or 98.6°F. The body core temperature and the blood volume are normal.
Just a few points on blood volume before we move on: Blood has a fluid component called plasma and a cellular component which are the red and white blood cells. 80% of the blood volume is in the peripheral circulatory system and the other 20% is splanchnic blood in the vital organs. On average, an adult male who weighs 70 kg has a blood volume of about 5 liters.
Sweat is primarily water and electrolytes from the plasma. If you recall, I said that people can produce a maximum of 1 to 2 liters of sweat per hour. So its fair to say that sweating without fluid replacement will result in reduced blood volume.

## Slide 46: Physiology of Heat Stress
Hot weather, heat sources, and hard work raise the body core temperature. The body loses heat through:
Vasodilation
Sweating
CORE TEMP
BLOOD VOL
Normal
Notes: Under heat stress, the body core temperature rises in hot weather, in the presence of other heat sources, and during hard work. The body loses heat through:
Vasodilation where hot blood is pumped to the skin surface and cooled through radiant and convective cooling mechanisms and sweating where body moisture is released to the skin surface and evaporative cooling occurs. The core body temperature and blood volume are consistent.

## Slide 47: Physiology of Heat Stress
During heavy work, a body can lose 1-2 liters of water per hour.
Thirst is not stimulated until the body is already 1-2% dehydrated.
Desire to drink fluids diminishes with increased core temperature.
Involuntary Dehydration
CORE TEMP
BLOOD VOL
Normal
Normal
Notes: During heavy work, a body can lose 1-2 liters of water per hour. This water and any lost electrolytes must be replaced to maintain homeostasis.
If you are thirsty, then you are already experiencing mild dehydration. Thirst is not stimulated until the body is already 1-2% dehydrated.
Somewhat counterintuitive, is the fact that the desire to drink fluids diminishes with increased core temperature.
So dehydration is playing a role in lowering the blood volume.

## Slide 48: Physiology of Heat Strain
A dehydrated person may experience:
Headaches
Loss of accuracy/dexterity
Muscle fatigue and cramping
Weakness
Reduced Alertness
Nausea
Increased Heart Rate
CORE TEMP
BLOOD VOL
Normal
Normal
Low
Notes: The longer a body sweats, the less blood there is to carry heat to the surface of the skin and carry oxygen and nutrients to muscles. The body is straining to maintain homeostasis.
Maintaining a high skin blood flow with lower blood volume strains the cardiovascular system and the heart during physical work in the heat. Because blood is pooling near the skin surface less blood is available for oxygenation and circulation to vital organs. So your heart rate increases to maintain cardiac output.
For these conditions the primary cardiovascular challenge is to have sufficient cardiac output to simultaneously support high skin blood flow for heat dissipation and high muscle blood flow for metabolism. The body further compensates by diverting blood flow from internal organs to skin and muscle.
The reduction in blood flow to vital organs, if excessive, can contribute to the development of heat related injury. (TB MED 507/AFPAM 48-152)

## Slide 49: Heat Stress -> Heat Strain Heat Related Illness
The early symptoms of heat exhaustion include:
Profuse sweating
Muscle cramps
Fatigue
Thirst
Heat rash or
Prickly Heat
http://www.nlm.nih.gov/medlineplus/ency/article/000056.htm
Notes: So far we have covered heat stress and heat strain. There are a variety of symptoms associated with heat stress and heat strain. For the sake of time, I have grouped symptoms into early and late stage symptoms of heat exhaustion. There is no particular order in which these symptoms may appear and not all of the symptoms have to be present in order to conclude that a person is experiencing a heat related illness.
Acclimated people sweat more efficiently, reserving electrolytes in their bodies. Sweating in unacclimated persons may be profuse and full of electrolytes that the body requires. Lack of electrolytes may result in painful muscle cramps or spasms. It is important to understand that cramps can be caused by too much or too little salt
Fatigue is a state of increasing discomfort and decreased efficiency due to prolonged or excessive exertion; it is the loss of power or capacity to respond to stimulation.
Thirst is signaled when the body is 1-2% dehydrated. If you are thirsty, you are already mildly dehydrated.
Heat rash or Prickly Heat is manifested as red papules and usually appears in areas where the clothing is restrictive. It occurs in skin that is persistently wetted by un-evaporated sweat. Heat rash papules may become infected if they are not treated. Damaged skin may contribute to increased dermal uptake of contaminants.
Paying attention to the early signs and symptoms of heat strain are important in preventing more serious heat related illness. Acclimatization and hydration/electrolyte replacement are important measures in the prevention of the later symptoms of heat exhaustion.
https://www.google.com/search?q=sweat+and+thirst+images&hl=en&qscrl=1&rlz=1T4ADFA_enUS427US428&tbm=isch&tbo=u&source=univ&sa=X&ei=lUNDU-KJLbKqsQTf3YCQCQ&ved=0CD8Q7Ak&biw=1920&bih=992#facrc=_&imgdii=_&imgrc=d5vS7jtgizsULM%253A%3BuI7d5U7UIukIVM%3Bhttp%253A%252F%252Fimages.theage.com.au%252F2012%252F11%252F09%252F3782091%252Fml_drink_wide_20121109120648602123-300x0.jpg%3Bhttp%253A%252F%252Fwww.theage.com.au%252Fexecutive-style%252Ffitness%252Fblogs%252Fthe-long-run%252Fthirsty-work-20121109-29275.html%3B300%3B258

## Slide 50: Heat Related Illness
Later symptoms of heat exhaustion include:
Headache
Dizziness and lightheadedness
Weakness
Nausea and vomiting
Cool, moist skin
Dark urine
Fainting or Passing out
Notes: Symptoms with later onset are typically the result of prolonged heat exposure and increasing dehydration:
As Gavin indicated, Dizziness and fainting associated with heat exhaustion can be dangerous because the victim may be in a hazardous environment where clumsiness, weakness, disorientation and loss of consciousness may result in serious or life threatening injuries due to being caught in or struck by operating machinery, motor vehicles or as the result of falls.
Symptoms of heat exhaustion include:
Headaches,
dizziness/light headedness,
Mood changes (irritable, or confused/can’t think straight)
Nausea,
vomiting
Decreased and dark-colored urine,
pale clammy skin
and pupils may become dilated.
The victim is usually conscious but may faint if they have a core temperature of over 102°F.
http://blogs.cdc.gov/niosh-science-blog/files/2012/07/pdsicklv.jpg

## Slide 51: Heat Related Illness
Heat Syncope
Sudden loss of consciousness associated with fainting or passing out.
Blood pressure drops, oxygenated blood supply to the brain is low, and
The onset of syncope is rapid and unpredictable.
Credit: B. Mizula
Notes: The medical term for fainting is syncope.
In heat syncope, the brain does not receive enough oxygen because blood pressure drops and blood pools in the legs or extremities resulting in fainting.
The onset of heat collapse is rapid and unpredictable but generally recovers within a few seconds as blood pressure is restored. However, if a victim experiences heat syncope in a dangerous location, the results could be fatal.
https://www.osha.gov/SLTC/heatstress/index.html

## Slide 52: Heat Related Illness
The symptoms of Heat Stroke include:
High Fever
Irrational behavior
Extreme confusion
Dry, hot, and red skin
Rapid, shallow breathing
Rapid, weak pulse
Seizures
Unconsciousness
Notes: Heat stroke occurs when the body's system of temperature regulation fails and body temperature rises to critical levels
This condition is caused by a combination of highly variable factors, and its occurrence is difficult to predict
The symptoms of heat stroke include:
Confusion,
irrational behavior,
loss of consciousness,
convulsions
Lack of sweating
hot, dry skin, (new evidence suggests a victim may be moist);
and an abnormally high body temperature, e.g., an internal temperature of 105.8° F
Pulse is strong and rapid
Small pupils
If body temperature is too high, it can cause death or other permanent impairment.
Photo: Microsoft clip art

## Slide 53: Heat Stroke is a Medical Emergency
Call 911
Begin cooling immediately
Notes: Heat Stroke is a Medical Emergency
Call 911 if:
The person loses consciousness at any time.
There is any other change in the person's alertness (for example, confusion or seizures).
The person has a fever over 102 °F.
Other symptoms of heatstroke are present (like rapid pulse or rapid breathing).
The person's condition does not improve, or worsens despite treatment.
Begin administering first aid to cool the victim.
Place the worker in a shady area and remove the outer clothing.
The worker's skin should be wetted and air movement around the worker should be increased to improve evaporative cooling until professional methods of cooling are initiated and the seriousness of the condition can be assessed. Fluids should be replaced as soon as possible. Never give an unconscious person fluids.
Decreasing body core temperature below 38.9°C (102°F) within 30 minutes of presentation of heat stroke improves survival.
Make sure you know where you are so you can get the help you need from Emergency Service Providers. Know the address of your location or the names of the nearest intersecting streets.
The bottom lines is: Do NOT underestimate the seriousness of heat related illnesses.
H sign Microsoft clip art
Ambulance interior courtesy of Dean Bowman

## Slide 54: Clinical Features of Heat Stroke
Cardiovascular
Neurological
Acid-Base Disturbance
Kidney
Gastrointestinal
Hematological
Immunological
Muscular
Grogan and Hopkins,, Heat Stroke: Implications for Critical Care and Anaesthesia
British journal of Anaesthesia 88 (5): 700-7 (2002)
Notes: The two cardinal features of heat stroke presentation are: raised body temperature and neurological dysfunction. Because multiple organ systems are involved , there are clinical features in a number of systems:
Cardiovascular features of heat stroke include hyperdynamic circulation with elevated heart rate and high cardiac output. Low blood volume was observed in stroke victims and interestingly, signs of peripheral vasoconstriction (whereas heat exhaustion patients were more likely to have vasodilation).
Additionally all components of the Electrocardiogram can be affected including rhythm disturbances, conduction defects, prolongation of the Q-T Interval and ST segment changes. In one study 21% of heat stroke patients showed these changes.
Neurological: Impairment may be of varying degrees and duration. These include bouts of delirium, lethargy, coma and seizures. In a case study reported by Albukrek, et al, Cerebellar atrophy was observed in a 45-year old man 10 weeks after his hyperthermic insult and worsened throughout the following year. Other cases included brain hemorrhage. Data from patients evaluated after the 1995 Chicago heat wave resulted in 24% of patients with no neurological impairment, 43% with minimal impairment but 33% had moderate to severe impairment function upon discharge from the hospital.
Acid – Base Disturbance and Plasma Composition Features described by Dematte and colleagues found that 45% of their patients had acid-base abnormalities. 60% of their patients required mechanical ventilation and 10% developed acute respiratory distress symptoms.
In the Kidney: The incidence of acute renal failure in exertional heat stroke is approximately 30%. Renal insufficiency has been reported in 53% of patients with classical heat stroke and 19% of that subset died.
Gastrointestinal features include: Abnormal liver function tests that peak approximately three days after insult. Liver damage is almost always seen and is properly related to direct thermal injury and hypoxia secondary to blood flow from visceral organs to the peripheral circulatory system. Liver failure is rare.
Hematological features in the Chicago heat wave cohort revealed that 45% of the cohort had evidence of coagulopathy.
Immunological features: This is quite striking: The pathophysiology of heat stroke has many similarities with sepsis syndrome. When blood is redistributed from the visceral organs to the periphery in an attempt to lose heat and supply skeletal muscle, there is a risk of gut ischemia. This facilitates the absorption of bacterial endotoxins. Blood purification therapy may be required.
Muscular features: It is the break down of muscle tissue where muscle fiber is released to blood and filtered in the kidneys causing damage.
http://www.westernu.edu/osteopathy/osteopathy-academics/osteopathy-curriculum/

## Slide 55: Prognosis After Heat Stroke
Temperature
Cardiovascular
Biochemical Markers
Disability at Discharge from Hospital
Notes: As with other groups of critically ill patients, there is no one marker that predicts outcome. But temperature, cardiovascular circulation, biochemical markers and disability at discharge appeared to be the most important indicators of outcome.
With Temperature: Decreasing temperature below 102 °F in the first 30 minutes improves survival. However, tissue injury can continue to develop after cooling to normal body temperature in 25% of patients suggesting activation of mediators (endotoxins, cytokines, injured endothelium, and activated coagulation factors)
Patients with Cardiovascular effects present with hyperdynamic or hypodynamic circulation. Patients with hypodynamic circulation present with circulatory failure and have a poorer outcome.
With Biochemical Markers: Concentrations of biomarker for muscle damage and liver function concentrations were higher at the time of admission in heat stroke survivors than the non-surviving group and the severely ill group than those who had a quick recovery. The enzyme with the highest prognostic accuracy for survival versus death was total LD, followed by CK, AST and ALT.
Disability at discharge: In-hospital mortality rate for heat stroke is 21% . 1/3 of patients at discharge have moderate to severe functional impairment which may be prolonged. The degree of functional disability correlated highly with 1-year survivability. At 1 year, a further 28% of patients had died.

## Slide 56: Prevention
Photo: M. Twilley
Notes: So how do we prevent heat related illness on the job.

## Slide 57: Heat Related Illness Prevention Programs
Generally consist of:
Worker Training/Awareness
Provisions for acclimating workers to heat
Reduction of physical demands
Provide water breaks in cool rest areas
Worker and environmental monitoring
Work/Rest schedules
Avoidance through alternative work schedules
Notes: Public Health advisories for the prevention of heat related illnesses include recommendations to wear loose-fitting, lightweight clothing, to rest frequently and seek shade, avoid exercise and strenuous activity outside, drink plenty of fluids and avoid overheating.
Workplace environments pose special challenges in heat related illness prevention. Worker protection is accomplished through awareness training, acclimatization through longer periods of work in hot environments, reducing physical demands on workers, providing opportunities for hydration, providing cool rest areas in which to take breaks, perform monitoring or avoiding work in heat stress conditions.

## Slide 58: Acclimatization
ACGIH: The gradual physiological adaptation that improves an individual’s ability to tolerate heat stress conditions.
Noticeable loss after 4 days
Complete loss after 4 weeks
Notes: According to the ACGIH: A worker can be considered acclimatized with a history of heat-stress exposure of at least two continuous hours a day in 5 out of last 7 days or 10 out 14 days. Acclimatization can be lost in as few of 4 days.
The chart shown is from NIOSH in which gradual acclimatization occurs more quickly in experienced heat workers than in new workers, but in general both populations achieve acclimatization in about 5 days.
People will not be fully acclimatized to sudden higher levels of heat as would be the case in a heat wave or the introduction of a new heat producing process.

## Slide 59: Acclimatization
Thermal Comfort | Exercise Performance
Core Temperature – Reduced Sweating Efficiency – Improved Earlier Onset Higher Rate Redistributed Sweat Output Skin Blood Flow – Improved Earlier Onset Higher Rate Metabolic Rate - Lowered | Cardiovascular Stability – Improved Heart Rate – Lowered Stroke Volume – Increased Blood Pressure – better Defended Myocardial Compliance – Improved Fluid Balance – Improved Thirst – Improved Electrolyte Loss – Reduced Total Body Water – Increased Plasma (Blood) Volume – Increased and Better Defended
Table 2.1 - Actions of heat acclimation from Army TB MED 507
Notes: One of the key concepts in heat stress management is worker acclimation to hot environments. Acclimatization or acquired thermal tolerance refers to cellular adaptations induced by heat exposure that protect tissue and organs from heat injury. This tolerance is associated with heat shock proteins (HSP) which provide protection and accelerate repair of cells from heat exposure and stressors.
ARMY TB Med 507 (Table 2.1) shows the physiological benefits to heat acclimatization. The table lists improvements in thermal comfort factors associated with core temperature, sweating efficiency, skin blood flow and metabolic rate. It also illustrates exercise performance in terms of cardiovascular and fluid balance factors.

## Slide 60: Heat Index
OSHA: Using the Heat Index: A Guide for Employers
https://www.osha.gov/SLTC/heatillness/heat_index/index.html
Notes: Guidance on heat stress management is available from OSHA and ACGIH. This OSHA guidance titled Using the Heat Index: A Guide for Employers is advisory in nature and informational in content. Pursuant to the OSH Act, General Duty Clause, Section 5(a)(1), OSHA requires employers to provide their employees with a workplace free from recognized hazards likely to cause death or serious physical harm. With the volume of information on the OSHA website and regional emphasis programs in the US, Heat Illness Prevention programs certainly fall under the General Duty Clause.
The Guide promotes the use of the Heat Index published by the National Weather Service. Color coded combinations of Temperature and Relative Humidity are grouped into four categories of caution, extreme caution, danger and extreme danger. Temperature and Relative Humidity are easy to measure and are widely available from a variety of media sources.
It is IMPORTANT NOTE that The heat index values were devised for shady, light wind conditions, and exposure to full sunshine can increase heat index values by up to 15° Fahrenheit. To account for solar load, added precautions are recommended. We will briefly explore the protective Measures to Take at Each Risk Level in the next two slides.
Strenuous work and the use of heavy or specialized protective clothing also have an additive effect. As a result, the risk at a specific heat index could be higher than that listed in the table above if the work is in direct sunlight, without a light breeze, or if work involves strenuous tasks or the use of heavy or specialized protective clothing. Extra measures, including implementing precautions at the next risk level, are necessary under these circumstances.

## Slide 61: Heat Index
Heat Index | Risk Level | Protective Measures
<91°F | Lower (Caution) | Provide drinking water Ensure available medical resources Plan ahead for higher heat indices Encourage use of sunscreen
91°F to 103°F | Moderate | In addition to the steps listed above: Remind workers to drink water often Review heat-related illness topics with workers Schedule frequent breaks in cool, shaded area Acclimatize workers Set up buddy system/watch workers fro signs of heat-related illness.
Notes: The most critical actions employers should take to help prevent heat-related illness at each risk level are shown on the table. In the lower risk or caution level with a heat index less than 91°F, employers are encouraged by OSHA to provide drinking water, ensure medical resources are available if needed, start planning for higher heat indices including conducting heat safety training, and encourage workers to wear sunscreen. If workers must wear heavy protective clothing, perform strenuous activity or work in the direct sun, additional precautions are recommended to protect workers from heat-related illness.
At the moderate heat index range of 91-103°F, additional steps are recommended by OSHA. These include drinking about 4 cups of water an hour, conduct a review of heat related illness topics with workers, schedule frequent breaks in cool, shaded areas, acclimate workers to heat, and set up a buddy system/surveillance for heat related illness.

## Slide 62: Heat Index
Heat Index | Risk Level | Protective Measures
103°F to 115°F | High | In addition to the steps mentioned previously: Alert workers of high risk conditions Actively encourage workers to drink plenty of water Limit physical exertion Have person well-informed about heat related illnesses determine appropriate work rest schedule Establish and enforce work rest schedules Adjust work activities Use cooling techniques Watch/communicate with workers at all times
>115°F | Very High to Extreme | Reschedule work If essential work must be performed: Move work tasks to coolest part of the shift Conduct physiological monitoring Develop and enforce protective work/rest schedules Stop work if controls are not working
Notes: As the heat index severity increases, so do the corresponding recommended protective measures. In high risk and extremely high risk circumstances, OSHA recommends rescheduling the work to cooler time periods including working at night.

## Slide 63
Notes: OSHA includes this table from the Army Public Health Command in the “Using the Heat Index: A Guide for Employers” as an example of a method for Developing Work/Rest Schedules
This table is used for setting work/rest schedules during military field operations. The hydration and work/rest schedule assume an average sized, heat acclimated soldier wearing battle dress uniforms (BDU). Factors such as lack of acclimatization, poor fitness, and cumulative inadequate hydration that may increase the risk of heat-related illness should be taken into account when using the schedules in this Figure.
This is one method for determining work/rest schedules using the Wet-Bulb Globe Thermometer Temperature (WBGT). The WBGT meter provides a heat reading incorporating temperature and relative humidity part of the heat index, but also considers solar load (radiant heat, from sunshine) as well as how quickly moisture evaporates. WBGT meters are readily available from commercial sources of environmental monitoring. Several hand-held models cost less than $200 (in 2011).
The text on the right hand side of the table provides adjustment values for the WBGT indices based upon the use of body armor and protective clothing. MOPP (Mission Oriented Protective Posture) reflects full protective gear used by military personnel in a toxic environment that may consist of nuclear, biological or chemical threats. Similar to Level B or C PPE used in Hazardous Waste Operations.

## Slide 64: ACGIH TLV and Action Level
Threshold Limit Value (TLV) represents conditions under which it is believed that heat acclimatized, adequately hydrated, unmedicated, healthy workers may be repeatedly exposed without adverse health effects.
The Action Level is similarly protective of unacclimatized workers and represents conditions for which a heat stress management program are offered.
Notes: The ACGIH TLV and Action Level are intended to maintain the core body temperature within 1°C of normal.
The TLV represents conditions under which it is believed that heat acclimatized, adequately hydrated, unmedicated, healthy workers may be repeatedly exposed without adverse health effects.
The Action Level is similarly protective of unacclimatized workers and represents conditions for which a heat stress management program are offered.

## Slide 65: ACGIH Decision Logic
Does clothing allow for air or water vapor movement?
Yes No
Photo: D. Twilley www.niehs.nih.gov
Notes: The decision logic goes as follows:
Does clothing allow for air or water vapor movement?
Yes or no.

## Slide 66: Clothing Adjustment Factors
Clothing Type | Addition to WBGT (°C)
Work clothes (long sleeve shirt and pants ) | 0
Cloth coveralls | 0
Double -layer woven clothing | 3
SMS polypropylene coveralls | 0.5
Polyolefin coveralls | 1
Limited-use vapor-barrier coveralls | 11
Notes: If the answer to the first question is no. We have to add the clothing adjustment factor to the WBGT measurements before proceeding to the next step.

## Slide 67: TLV Screening Values (Acclimatized Worker)
Allocation of Work | Light TLV (WBGT °C) | Moderate (WBGT °C) | Heavy (WBGT °C) | Very Heavy (WBGT °C)
Metabolic Rate (W) | 180 | 300 | 415 | 520
75-100% | 31.0 | 28.0 | --- | ---
50-75% | 31.0 | 29.0 | 27.5 | ---
25-50% | 32.0 | 30.0 | 29.0 | 28.0
0-25% | 32.5 | 31.5 | 30.5 | 30.0
Notes: Which is comparing the WBGT value to the screening table. Table 2 in the TLV book actually establishes Screening Criteria for TLV and Action Limit using WBGT measurements for Heat Stress Exposure based upon the allocation of work in a cycle of work and recovery or rest. This table is frequently used incorrectly. This table is purely intended as a screening tool to evaluate whether a heat stress situation may exist as an input variable in the Heat Stress Decision logic. The table presents natural or prescribed rest breaks within an hour of work. It is more protective and therefore not intended to prescribe work and recovery periods. Actual TLVs and Action Levels are a function of WBGT temperature (°C) and metabolic rate expressed in Watts (W). Metabolic rate at rest is 115 W. Metabolic rates for light work, moderate work, heavy work and very heavy work correspond to 180, 300, 415 and 520 W respectively.
So if your work force is expected to walk normally or do light pushing and pulling tasks, they would fall into the moderate work category. If they sustain that activity for 80% of the hour, the screening WBGT temperature is 28.0°C without adjusting for clothing.
The decision logic asks: Are Screening criteria in Table 2 Exceeded? In order to answer this question, you have to know the WBGT temperature. The answer would be yes if the WBGT temperature is at or above 28°C.
Say the workers are wearing polypropylene coverall during their moderate activity. Add the clothing value to the WBGT temperature then compare to the screening value.
You see the table cells where dashes fill the space. ACGIH does not recommend using screening criteria for these categories. Instead, detailed analysis or physiological monitoring should be used. Methods for performing the detailed analysis are presented in the TLV Documentation and other sources.
Once you complete the screening, you decide whether excessive heat strain will occur. If so, physiological monitoring is used to limit heat strain.

## Slide 68: Physiological Monitoring
Heart Rate
Sustained HR > 180 bpm – age in years
Recovery HR at 1 min >120 bpm
Core Temperature
Acclimatized: > 38.5°C
Unacclimatized: > 38.0°C
Weight Loss
> 1.5% of body weight over a shift
Notes: This slide presents examples of physiological monitoring that are easy to do yourself. These are measures that mark excessive heat strain can be incorporated in your heat stress program.
The first is to take heart rate measurements. If you have ever participated in group aerobic fitness classes, you probably already know how to do this. All you need is watch or timer and two fingers. Find your carotid artery pulse and count the heart beat for 15 seconds. Multiply by 4 to get beats per minute. Then subtract your age from your heart rate. If the number exceeds 180 bpm then you are experiencing excessive heat strain. You can also check your heart rate one minute after peak work. If the count is greater than 120 bpm then you need to take measures to rest and control heat exposure.
Core temperature is another measure that we can use during work but the traditional way of obtaining core temperature is through the use of a rectal thermometer. Other measurement devices can be used like tympanic thermometers that are less awkward to use on the job. I will also share with you a few other techniques for monitoring core temperature in a couple of minutes.
Weight loss is easily measured using a portable scale and calculating the percent loss of body weight at the end of the day. If the percentage loss is more than 1.5% of body weight then heat strain is suspected. In practicality, a 70 kg (154 lb adult) would have to lose 1.05 kg (2.3 lbs) in one day to be considered under heat strain.
Of course, if you have any symptoms of heat strain, no matter what the physiological field monitoring indicates, please take preventive measures.

## Slide 69: Dehydration
http://www.nlm.nih.gov/medlineplus/ency/imagepages/17223.htm
Notes: Skin turgor testing is an indication of dehydration. If you recall, I said early in the presentation that thirst is triggered with the body is 1-2% dehydrated. This test is simple to perform and can be done on the back of the hand or the abdomen. Pinch the skin between your fingers to make a ridge. Hold it for a few seconds and release the skin. If the skin remains elevated and doesn’t snap back into place, then 5-10% dehydration is suspected. This method doesn’t work well with older crepe skin.

## Slide 70: Monitoring Tools
Notes: I mentioned a couple of techniques for measuring core temperature. The aptly named CoreTemp sensor was developed here at the JHU APL in collaboration with NASA
In the mid-1980’s. In 1991, the CorTemp sensor technology made its debut in space, where it was ingested by astronauts so their core body temperature could be monitored and relayed via radio frequency signals to computers back on earth.
The silicone coated sensor contains a micro battery, quartz crystal, communication coil and circuit board, all encapsulated in medical grade epoxy. Once ingested, the crystal sensor vibrates at a frequency relative to the body’s internal temperature, produces a magnetic flux and transmits a low-frequency signal harmlessly through the body.
The sensor passes through the body at the subject’s normal rate of motility which can vary anywhere from 24-36 hours. Monitoring can be extended by administering another sensor after the initial pill has passed. The CorTemp® sensor is accurate to ± 0.1°C and is FDA cleared and registered as a single use device.

## Slide 71: Monitoring Tools
Notes: The SafetySpot personal monitoring sensor utilizes multiple patent-pending technologies that estimate core body temperature from two locations: the carotid artery just below the ear, and the temporal artery region across the temple to just above the eyebrow. If the users estimated core temperature rises above 103F for more than 45 seconds the sensor will activate. – Once activated, the alarm will transmit an audible beep and flash a red LED for a period of 30 seconds until the users estimated core temperature returns below the alarm threshold. - See more at: http://sportandindustrysafetydevices.com/?page_id=209#sthash.pGG6XxvY.dpuf
See more at: http://sportandindustrysafetydevices.com/?page_id=209#sthash.pGG6XxvY.dpuf

## Slide 72: Monitoring Tools
Notes: Thermal imaging for screening traveling populations for pandemic flu outbreak made the news during the HIN1 scare a few years ago and it appears that thermal imaging cameras may become a useful tool in heat stress monitoring.
A recent study by Bourlai et all of wildland firefighters had encouraging results based on the small population that they screened.
By way of disclaimer, I do not endorse or promote any of the these items. They were easy found through general search terms on the web. I’m sure there are many more tools to use in our tool box that I can keep talking about them all day. For now, I will turn the presentation back over the Gavin West so he can share with you some of the great solutions that are available for controlling heat stress. Thank you.
One study titled Use of thermal imagery for estimation of core body temperature during precooling, exertion, and recovery in wildland firefighter protective clothing.

## Slide 73: Control Technologies and Informational Resources for Preventing HRIs
Gavin West, MPH
Research Analyst, CPWR
Notes: Thanks so much, Michele, for your thoughtful explanation of the physiological and more technical aspects of heat stress, heat strain, and heat-related injuries.

## Slide 74
Image by NIOSH via Wikimedia Commons
Notes: I’m sure all of you are familiar with the hierarchy of controls.
I’d like to spend the next portion of the talk discussing control technologies for preventing HRI in the context of this hierarchy.

## Slide 75: Unless you know of a way to eliminate or substitute the sun, let’s move on to engineering controls

## Slide 76: That was actually my attempt at a joke, but let me pose this question to you
Can you think of any methods of substitution or elimination to reduce heat exposure?
  Think about Prevention through Design
  Consider substituting work practices or equipment that generate excess heat for those that do not

## Slide 77: OSHA recommends the following engineering controls
A/C (construction equipment cabs, e.g.)
Increased general ventilation
Cooling fans
LEV @ points of heat or moisture production
Reflective shields to redirect radiant heat
Insulation of hot surfaces (furnace walls, e.g.)
Elimination of steam leaks
Notes: LEV = Local Exhaust Ventilation

## Slide 78: For example, misting fans and A/C units such as the ones shown here
Notes: Image of Big Fogg Cool Blue Misting Fan from CPWR Construction Solutions website.
Image of MovinCool OfficePro24 Portable Air Conditioner from CPWR Construction Solutions website.

## Slide 79: Administrative controls are also critical for preventing HRI
Emergency planning
Acclimatization
Access to water, shade, rest areas
Work/rest scheduling
Rotating workers to minimize overexertion
Monitoring workers
Buddy system
Training & education
Notes: We’ve stressed acclimatization, but water, rest, and shade are equally important and have been a major focus of OSHA’s nationwide campaign to prevent HRI.
A 2003 study of underground mine workers found that “involuntary dehydration” did not occur in well informed workers (Brake & Bates, 2003), which underscores the importance of training and education.
“Involuntary dehydration” is the delay in full restoration of a body water deficit by drinking.

## Slide 80: For example, scheduling work during cooler parts of the day or season
“Night work” courtesy DOT
Slide content courtesy Bernard Mizula

## Slide 81: PPE is a last resort in the hierarchy of controls but still important
Personal cooling systems
Reflective clothing
Ice vests
Wetted clothing
Water-cooled garments
Garments w/ circulating cooled air
Notes: Don’t forget that PPE can also be a significant risk factor for HRI.

## Slide 82: I encourage you to explore additional resources
Notes: I strongly encourage you to explore additional resources to help you develop effective strategies for preventing HRI.
Let’s review some of what’s out there.

## Slide 83: OSHA has great material on their campaign website
https://www.osha.gov/SLTC/heatillness/
Notes: In 2010, Cal/OSHA initiated a statewide education campaign to reduce heat-related illnesses and fatalities and increase awareness of California’s heat standard requirements.
As Michele mentioned, there is no Federal OSHA Standard that is specific to heat stress.
Popular education, organizational capacity building, and community-based outreach using community health promoters or promotores were key components of the CA campaign (Riley et al., 2012).
Success of the campaign in CA helped to bring about OSHA's nationwide Heat Illness Prevention Campaign.
Tons of useful educational, training, and other materials are available on their campaign website.

## Slide 84: You may be particularly interested in OSHA’s smartphone app
Use on iPhone & Android
Calculate heat index
Display risk level
Specify protective measures at that risk level
https://www.osha.gov/SLTC/heatillness/heat_index/heat_app.html
Notes: “The App allows workers and supervisors to calculate the heat index for their worksite, and, based on the heat index, displays a risk level to outdoor workers.
Then, with a simple "click," you can get reminders about the protective measures that should be taken at that risk level to protect workers from heat-related illness.”

## Slide 85: Visit their S&H Topics page with industry-specific resources
https://www.osha.gov/SLTC/heatstress/index.html
Notes: Industries covered are: Agriculture, Baggage Screeners, Construction, Emergency Response and Cleanup, Foundries, Health Care, Military, Mining, Oil and Gas.

## Slide 86: NIOSH is a reliable source for heat stress materials
http://www.cdc.gov/niosh/topics/heatstress/
Notes: The page shown here also has a comprehensive list of government and additional resources, such as a link to purchase the ACGIH TLV.
NIOSH will be releasing a new guidance document on heat stress to update their prior version from 1986.
A public meeting for comment on the draft criteria document was held on February 13, 2014.
You can access the draft criteria document and related materials via the website and URL shown on this slide.
As of now, updated topics in the draft document include hydration and fluid requirements, body fat, obesity, medications, caffeine usage, exertional heat stroke, HHE reports, case studies, and physiological monitoring among other updated items.
This will be a comprehensive and very useful document, so be sure to keep an eye out for the final version to be released in the near future.

## Slide 87: Beyond collecting good data, the military also provides thorough OHS guidance
http://www.usace.army.mil/SafetyandOccupationalHealth/SafetyandHealthRequirementsManual.aspx
Notes: The US Army Corps of Engineers’ Safety and Health Requirements Manual, also known as the EM 385, has an informative section on heat and cold stress management.
It’s available at no cost online.

## Slide 88: CPWR offers free toolbox talks, including one for heat stress
http://www.cpwr.com/publications/handouts-toolbox-talks
Notes: I hope you don’t view this as shameless self-promotion because I believe that CPWR, the non-profit organization I work for, offers materials that can help protect workers from the hazards of heat exposure.
These materials are available at no cost.

## Slide 89: CPWR’s elcosh covers heat stress
http://www.elcosh.org/
Notes: CPWR has another website called elcosh, which is short for electronic library of construction occupational safety & health.
This a screen shot of the elcosh homepage, where one can access free information and guidance on heat stress by browsing the hazards category and clicking on ‘weather conditions’.
The toolbox talk I showed on the last slide can also be accessed here.

## Slide 90: CPWR’s Construction Solutions website is a practical tool
http://www.cpwrconstructionsolutions.org/
Notes: Last but not least, CPWR’s Construction Solutions website can be a practical tool.
The site provides hazard analysis by hazard, line of work, and task.
For example, a roofer could access a heat exposure hazard analysis for the task of installing an asphalt roof.
As the name implies, the site is primarily designed to provide solutions for construction hazards.
The solution partially shown on the left is a Heat Stress Program.
Shown on the right is part of a solution regarding the use of PPE for preventing heat stress.

## Slide 91: The site provides info on heat stress solutions and evidence-based reviews
http://www.cpwrconstructionsolutions.org/
Notes: You can find information regarding the personal temperature monitor, hard hat liner, or cooling vest shown here, among many other solutions.
CPWR does not endorse any products or brands, but the site does review relevant research findings to help users understand what is known about the efficacy of heat stress controls.
For example, some of the literature cited suggests that cooling vests can be effective, intermittent regional cooling such as water misting even more so, and that neck-cooling alone could be potentially dangerous for workers.
The statement made about neck-cooling is based upon a 2011 study by Tyler and Sunderland looking at athletic performance with and without the use of cooling collars.
Briefly stated, cooling the neck region enabled the study participants to push themselves farther than they would without the cooling collar, decreasing perceived thermal strain while increasing actual measurements of thermal strain on the body.
Excerpts from Construction Solutions website:
“In 1988, the NAVY conducted a study of cooling vests including one that uses frozen gel packs. This vest was tested through several parameters including: rectal and skin temperature, heart rate, oxygen uptake and sweat rate. During work activities in hot environments, the vest proved to keep all parameters at statistically significant lower thresholds than the controls (Pimental, 1992).”
“A research study completed in 2008 tested the effects of multiple personal cooling equipment devices on the alleviation of heat strain in high temperature work areas. There were eight testing conditions: the control (wearing no cooling products), neck cooling scarf “A”, neck cooling scarf “B”, frozen gel-pack brimmed hat, cooling vest and various combinations of these items. Results showed that rectal temperature was effectively maintained and overall skin temperature and heart rate became more stable when participants wore personal cooling equipment. Researchers concluded that the combination of the cooling vest, a cooling scarf, and the brimmed gel-pack cooling hat showed a considerable amount of heat stress elimination, with a total cooling area of 4.2% of the body surface area, compared to only 3.3% when just a vest was worn (Choi, 2008).”
“A more recent study indicated that cooling collars alone could actually increase the risk. Researchers tested the hypothesis that cooling the neck region improves exercise ability while working in hot environments. Athletes participating in the study completed four running tests inside an environmental chamber. The first set of participants wore a cooling-gel collar, while the second set of participants did not wear the collar. Time to exhaustion, heart rate, rectal temperature, neck skin temperature, rating of perceived exertion, and thermal sensation were measured. The researchers concluded that participants who wore the cooling-gel collars were able to exercise 13.5% longer on average before reaching their maximum level of exhaustion because the cooling collars dampened the perceived levels of thermal strain. Despite these perceptions of relief, their extended exertion did not reduce rectal temperatures or heart rates, potentially increasing the risk of heat-related illness (Tyler & Sunderland, 2011).”
“A 2003 study tested the hypothesis that intermittent regional cooling, i.e. water misting or local evaporative cooling of one area of the body, was more effective at increasing heat loss than constant cooling from techniques such as cool vests, during heat stress. Four different intermittent tests were conducted to cool off different parts of the body at different time intervals into the test. The intermittent cooling was 164-215% more efficient at removing heat from the body than the constant cooling test (Cheuvront, 2003).”

## Slide 92: References
Armed Forces Health Surveillance Center. Update: Heat injuries, active component, U.S. Armed Forces, 2010. Medical Surveillance Monthly Report (MSMR). 2011 March;18(3):6-8.
Atan L, Andreoni C, Ortiz V et al. High kidney stone risk in men working in steel industry at hot temperatures. Urology 2005;65(5):858-861.
Axelsson O. Influence of heat exposure on productivity. Work Environ Health. 1974;11:94–9.
Becker JA, Stewart LK. Heat-related illness. Am Fam Physician 2011;83(11):1325-1330.
Bonauto D, Anderson R, Rauser E, Burke B. Occupational heat illness in Washington State, 1995-2005. Am J Ind Med 2007;50(12):940-950.
Borghi L, Meschi T, Amato F, Novarini A, Romanelli A, Cigala F. Hot occupation and nephrolithiasis. J Urol 1993;150(6):1757-1760.
Bottomley TA, Roth EM. Compendium of human responses to the aerospace environment. 6. Thermal environment. NASA CR-1205(1). NASA Contract Rep NASA CR 1968;6-148.
Bourbonnais R, Zayed J, Levesque M, Busque MA, Duguay P, Truchon G. Identification of workers exposed concomitantly to heat stress and chemicals. Ind Health 2013;51(1):25-33.
Brake DJ, Bates GP. Fluid losses and hydration status of industrial workers under thermal stress working extended shifts. Occup Environ Med 2003;60(2):90-96.
Cheuvront SN, Kolka MA, Cadarette BS, Montain SJ, Sawka MN. Efficacy of intermittent, regional microclimate cooling. J Appl Physiol (1985 ) 2003;94(5):1841-1848.

## Slide 93: References continued
Choi JW, Kim MJ, Lee JY. Alleviation of heat strain by cooling different body areas during red pepper harvest work at WBGT 33 degrees C. Ind Health 2008;46(6):620-628.
Crandall CG, Gonzalez-Alonso J. Cardiovascular function in the heat-stressed human. Acta Physiol (Oxf) 2010;199(4):407-423.
Epstein Y. Heat intolerance: predisposing factor or residual injury? Med Sci Sports Exerc 1990;22(1):29-35.
Ganio MS, Overgaard M, Seifert T et al. Effect of heat stress on cardiac output and systemic vascular conductance during simulated hemorrhage to presyncope in young men. Am J Physiol Heart Circ Physiol 2012;302(8):H1756-H1761.
Grogan H, Hopkins PM. Heat stroke: implications for critical care and anaesthesia. Br J Anaesth 2002;88(5):700-707.
Gubernot DM, Anderson GB, Hunting KL. The epidemiology of occupational heat exposure in the United States: a review of the literature and assessment of research needs in a changing climate. Int J Biometeorol 2013.
Hyatt OM, Lemke B, Kjellstrom T. Regional maps of occupational heat exposure: past, present, and potential future. Glob Health Action 2010;3.
Jackson LL, Rosenberg HR. Preventing heat-related illness among agricultural workers. J Agromedicine 2010;15(3):200-215.
Katsouyanni K, Pantazopoulou A, Touloumi G et al. Evidence for interaction between air pollution and high temperature in the causation of excess mortality. Arch Environ Health 1993;48(4):235-242.
Maeda T, Kaneko SY, Ohta M, Tanaka K, Sasaki A, Fukushima T. Risk factors for heatstroke among Japanese forestry workers. J Occup Health 2006;48(4):223-229.

## Slide 94: References continued
National Oceanic and Atmospheric Administration (NOAA) (2011) National Weather Service. Heat: a major killer. Available at: http://www.crh.noaa.gov/lmk/?n=noaaexcessiveheat Accessed: 17 March 2014
NIOSH. Criteria for a recommended standard: occupational exposure to hot environments. NIOSH Publication No. 86-113. Atlanta, GA: National Institute of Occupational Health; 1986.
Pimental NA, Avellini BA. 1992, Effectiveness of a selected microclimate cooling system in increasing tolerance time to work in the heat. Natick, MA: Navy Clothing and Textile Research Facility; Technical Report No. NCTRF 181.
Rainham DG, Smoyer-Tomic KE. The role of air pollution in the relationship between a heat stress index and human mortality in Toronto. Environ Res 2003;93(1):9-19.
Riley K, Delp L, Cornelio D, Jacobs S. From agricultural fields to urban asphalt: the role of worker education to promote California's heat illness prevention standard. New Solut 2012;22(3):297-323.
Sidhu P, Peng HT, Cheung B, Edginton A. Simulation of differential drug pharmacokinetics under heat and exercise stress using a physiologically based pharmacokinetic modeling approach. Can J Physiol Pharmacol 2011;89(5):365-382.
Tawatsupa B, Lim LL, Kjellstrom T, Seubsman SA, Sleigh A. Association between occupational heat stress and kidney disease among 37,816 workers in the Thai Cohort Study (TCS). J Epidemiol 2012;22(3):251-260.
Tyler CJ, Sunderland C. Cooling the neck region during exercise in the heat. J Athl Train 2011;46(1):61-68.

## Slide 95: References continued
Vanakoski J, Seppala T. Heat exposure and drugs. A review of the effects of hyperthermia on pharmacokinetics. Clin Pharmacokinet 1998;34(4):311-322.
Wild P, Moulin JJ, Ley FX, Schaffer P. Mortality from cardiovascular diseases among potash miners exposed to heat. Epidemiology 1995;6(3):243-247.
Xiang J, Bi P, Pisaniello D, Hansen A. Health Impacts of Workplace Heat Exposure: An Epidemiological Review. Ind Health 2013.
Yardley JE, Stapleton JM, Carter MR, Sigal RJ, Kenny GP. Is whole-body thermoregulatory function impaired in type 1 diabetes mellitus? Curr Diabetes Rev 2013;9(2):126-136.
Yardley JE, Stapleton JM, Sigal RJ, Kenny GP. Do heat events pose a greater health risk for individuals with type 2 diabetes? Diabetes Technol Ther 2013;15(6):520-529.

## Slide 96: We made it! Thanks so much for listening.
Image by: Joshbdork
via Wikimedia Commons

## Slide 97: Questions?
Michele M. Twilley, DrPH, CIH
President, Aria Environmental Inc.
Email: mtwilley@ariaenviro.com
Gavin H. West, MPH
Research Analyst, CPWR
Email: gwest@cpwr.com