## Slide 1
Health and Safety Hazards in Construction: Recognition, Control and Free Resources from CPWR
OH&S Webinar, June 20, 2018
Bruce Lippy, Ph.D., CIH, CSP, FAIHA
Director of Safety Research

## Slide 2: CPWR is a nonprofit established by North America’s Building Trades Unions
Research, training and service to improve safety and health in construction industry
National consortium with over 50 organizations
http://www.cpwr.com

## Slide 3: CPWR is funded by NIOSH, NIEHS and DOE
My comments are my own and don’t reflect policies or positions of NIOSH, NIEHS or DOE

## Slide 4: Construction is different
Decentralized and fragmented with mixed crafts
Highly cyclical
No fixed worksites
Changing environmental conditions
Extended hours in good weather
Travelers
Photo courtesy Miller and Long Co., Inc.

## Slide 5: Construction is dominated by small employers and a diverse workforce
90% have <20 employees
About 80% have <10 employees
30% of workers are Hispanic
14% are employed by temp agencies
Sources: U.S Census Bureau; CPWR Construction Chart Book 5th Edition; CPWR 2nd Quarter 2015 Quarterly Data Report

## Slide 6: Topics we will cover:
Fatality and injury data for the construction industry
Major hazards on construction sites
Managing and controlling construction hazards
Taking advantage of free CPWR resources

## Slide 7: Overview of fatalities and injuries in construction
Topic One

## Slide 8: Rate of deaths from injuries in construction, selected countries, 2008
ILO Data

## Slide 9: Rate of nonfatal injuries in construction, 2008. Why is the U.S. so low?
ILO Data

## Slide 10: Distribution of construction employment and work-related deaths from injuries, by establishment size, 2010. What is this saying?

## Slide 11: Small firms represent a disproportionate percentage of construction fatalities (2015)
CPWR The Chart Book 2018

## Slide 12: Distribution of fatal injuries in construction, by event, 2011-2013 total
Source: U.S. Bureau of Labor Statistics, 2011-2013 Census of Fatal Occupational Injuries. Numbers are from the online CFOI database.
Chart: Total = 2,486 fatalities
| Falls, slips, trips | Transportation | Contact w/ objects | Exposure | Other
 | 868 | 726 | 418 | 329 | 145

## Slide 13: Leading causes of work-related deaths, construction, 1992-2015

## Slide 14: Understanding the pattern of construction employment in the US is critical for interpreting S&H data, (BLS data 2003-2016)
Chart: Year
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
CPS
All Construction
Hispanic foreign-born
Hispanic native
Hispanic | 2.0705 | 2.2801 | 2.5773 | 2.9465 | 2.9797 | 2.6881 | 2.2603 | 2.2249 | 2.226 | 2.1609 | 2.3928 | 2.7052 | 2.8463 | 2.992
Non-Hispanic | 7.9958 | 8.4613 | 8.6004 | 8.7415 | 8.8665 | 8.2046 | 7.4301 | 6.8678 | 6.8311 | 6.7555 | 6.8644 | 7.1434 | 7.0914 | 7.339
 | 10.066 | 10.741 | 11.177 | 11.687 | 11.846 | 10.893 | 9.69 | 9.093 | 9.057 | 8.916 | 9.257 | 9.849 | 9.938 | 10.33
Source: U.S. Bureau of Labor Statistics, 2003-2016 Current Population Survey. Calculations by the authors.

## Slide 15: See any pattern in fatalities? (BLS)
Chart: Year
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Falls | 365 | 448 | 396 | 436 | 450 | 337 | 287 | 267 | 269 | 294 | 305 | 363 | 367
Other fatalities* | 806 | 830 | 847 | 861 | 789 | 679 | 592 | 535 | 512 | 555 | 551 | 570 | 618
 | 1171 | 1278 | 1243 | 1297 | 1239 | 1016 | 879 | 802 | 781 | 849 | 856 | 933 | 985
Note: In 2011, the CFOI switched to OIICS version 2.01 which categorizes slips, trips, and falls together. In previous years, slips and trips were categorized elsewhere.
* Other fatalities are fatalities from all causes except falls.
Source: U.S. Bureau of Labor Statistics, 2003-2015 Census of Fatal Occupational Injuries. Numbers were from the online CFOI database.
Notes: 15

## Slide 16: Construction had the most fatalities in 2016, although not the highest rate
Number of fatal work injuries
Fatal work injury rate (per 100,000 full-time equivalent workers)
U.S. BLS, Current Population Survey, Census of Fatal Occupational Injuries, 2017.

## Slide 17: The 10 occupations with highest fatal injury counts accounted for 39% of all fatal injuries in 2016
U.S. BLS, Current Population Survey, Census of Fatal Occupational Injuries, 2017.

## Slide 18: Rate of fatalities in construction has gone down dramatically for Hispanic workers (1992-2010)

## Slide 19: Except for the recent rate of fatal falls to a lower level (2011-2015, BLS)
Chart: Number of deaths per 100,000 FTEs
| 2011 | 2012 | 2013 | 2014 | 2015
Hispanic | 4.186 | 4.4065 | 4.1709 | 4.0066 | 4.8962
White, non-Hispanic | 2.6841 | 2.9085 | 2.819 | 3.4045 | 2.9789
All construction | 3.0015 | 3.2412 | 3.2239 | 3.5629 | 3.5572
Source: Numbers were obtained from the BLS through special requests. Numbers of FTEs were estimated using the Current Population Survey. Calculations by the authors. The views expressed here do not necessarily reflect the views of the BLS.

## Slide 20: Latino crew at the leading edge
Photos courtesy of Robert Carr

## Slide 21: Major Hazards on Construction Jobs
Topic Two

## Slide 22: Leading causes of work-related deaths, construction, 1992-2010

## Slide 23: Rate of leading causes of nonfatal injuries resulting in days away from work in construction, 1992-2010 (Private wage-and-salary workers)
OSHA revised requirements

## Slide 24
Falls

## Slide 25: Fatal falls, slips, trips in construction, by height of fall, 2011-2013 total
Note: 133 deaths without height information were excluded.
Source: These numbers were calculated by the authors with restricted access to BLS CFOI microdata. The views expressed here do not necessarily reflect the views of the BLS.
Chart: Total = 735 deaths
| Less than 6 feet | 6-10 feet | 11-15 feet | 16-20 feet | 21-25 feet | 26-30 feet | More than 30 feet
 | 0.082 | 0.11701 | 0.19728 | 0.17415 | 0.13878 | 0.095238 | 0.19592





## Slide 26: Distribution of fatalities from falls in construction, by establishment size, 2008-2010 total

## Slide 27: Rate of fatalities from falls, selected construction occupations, 2008-2010 average (All employment)
This research was conducted with restricted access to Bureau of Labor Statistics (BLS) data. The views expressed here do not necessarily reflect the views of the BLS.

## Slide 28: Over half of fatal falls to a lower level in construction were from roofs and ladders, 2011-2015 (BLS)
Source: Numbers were obtained from the BLS through special requests. Calculations by the authors.

## Slide 29: Number of fatal falls to a lower level, selected construction subsectors, 2011-2015
Chart: Year
| 2011 | 2012 | 2013 | 2014 | 2015
Nonresidential building | 23 | 23 | 19 | 25 | 24
Painting & wall covering | 20 | 25 | 26 | 34 | 19
Residential building | 26 | 46 | 40 | 52 | 61
Roofing contractors | 61 | 65 | 66 | 71 | 69
Source: Numbers were obtained from the BLS through special requests. Calculations by the authors. The views expressed here do not necessarily reflect the views of the BLS.

## Slide 30
What are “struck-by” hazards?

## Slide 31: Powder-actuated hand tools What are the hazards?
37,000 people go to emergency rooms from nail gun injuries every year
The hazards are similar to those of firearms
Sequential-trip triggers could prevent 65 percent of injuries
What is wrong with this picture?
Photo courtesy Laborers-AGC

## Slide 32: Pneumatic nailers have been made safer
Penetration checks must be made
All proper PPE must be worn

## Slide 33: Trenching cave-ins represent 40% of caught-in/between fatalities (2011-2015)
Notes: 33

## Slide 34: Dedicated to Patrick Walters
One of over 50 workers who needlessly die in trenching and excavation each year

## Slide 35: What do we know about the 542 “Patricks” who died in excavations from 1992 to 2001?
Average age was 38
Nearly half of their companies had less than 10 employees
Nearly all were employed by private companies
Cave-ins accounted for 76% of the deaths
Recovery of Patrick Walters’ body

## Slide 36: Lifetime risk of electrocution deaths in construction, selected construction occupations (All employment)
This research was conducted with restricted access to Bureau of Labor Statistics (BLS) data. The views expressed here do not necessarily reflect the views of the BLS.

## Slide 37: Major causes of electrocution deaths in construction, electrical workers vs. non-electrical workers, 2008-2010 total (All employment)

## Slide 38: Managing and Controlling Hazards on Construction Jobs
Topic Three

## Slide 39: Prevention through Design (PtD) promotes safety, but is not used much by smaller firms (average of 2012 and 2015)
Source: Dodge Data & Analytics, 2012 and 2015 Construction Safety Management Survey. Calculations by the authors.
Notes: 39

## Slide 40: CPWR’s Construction Solutions allows you to select a line of work and specific tasks to learn the hazards
www.cpwrconstructionsolutions.org

## Slide 41: Controls are listed for each hazard
Like stabilizers and extenders for ladders

## Slide 42: The hierarchy of controls needs to be considered
Electric wheelbarrow
Drywall lift
Overhead drill

## Slide 43: Here is why PPE is at the bottom
NIOSH FACE reports, fatal falls in construction, by Personal Fall Arrest System (PFAS) status, 1982-2014
Chart: Percent of fall fatalities
| 1982-1992 | 1993-2003 | 2004-2014
Present, in use | 0.0734 | 0.04 | 0.0732
Present, not in use | 0.2202 | 0.2571 | 0.1463
Not present | 0.6055 | 0.4914 | 0.5854
Unknown | 0.1009 | 0.2114 | 0.1951
Source: Dong XS, Largay JA, Choi SD, Wang X, Cain CT, Romano N. 2017. Accident Analysis & Prevention, 102:136-143.

## Slide 44: Frequency of general safety and health training, average of 2012 and 2015
Chart: Small: 1-9 employees
| Only when hired or required | Annually | Biannually | Quarterly | Other
1-9 employees | 0.3548 | 0.2419 | 0.1452 | 0.1935 | 0.0645
Chart: Large: 500+ employees
| Only when hired or required | Annually | Biannually | Quarterly | Other
500+ employees | 0.1538 | 0.183 | 0.0962 | 0.5192 | 0.0481
Source: Dodge Data & Analytics, 2012 and 2015 Construction Safety Management Survey. Calculations by the authors.

## Slide 45: Taking advantage of free CPWR resources
http://www.cpwr.com
Topic Four

## Slide 46: We worked with NIOSH to publish a series of toolbox talks (in English and Spanish)

## Slide 47: Our toolbox talks feature case studies and graphics

## Slide 48: Our safety climate tools are widely used

## Slide 49: Both versions focus on 8 leading indicators and have their own activities and ideas
Demonstrating Management Commitment
Aligning and Integrating Safety as a Value
Ensuring Accountability at All Levels
Improving Supervisory Leadership
Empowering and Involving Workers
Improving Communication
Training at All Levels
Encouraging Owner/Client Involvement

## Slide 50: Our Safety Climate Workbook contains worksheets that allow you to rate your program from inattentive to exemplary
“Management rarely comes to the actual jobsite.”
“Management integrates safety into every meeting...”

## Slide 51: The Small Contractor version allows you to quickly assess on paper or online your company’s activities and where you need help

## Slide 52: Our Hazard Alerts are in paper and digital form in English & Spanish

## Slide 53
Our electronic Library of Construction Occupational Safety and Health (eLCOSH.org) is focused on practitioners and trainers

## Slide 54: eLCOSH has over a thousand images for your use

## Slide 55: We maintain an inventory that currently contains 580 commercial construction nanomaterials
www.nano.elcosh.org

## Slide 56: Check out our other online resources & new safety and health network
www.stopconstructionfalls.com
www.choosehandsafety.org
  www.elcosh.org
SafeConstructionNetwork.org

## Slide 57: Our silica resources help contractors comply (www.silica-safe.org)

## Slide 58: We have lots of silica resources in English and Spanish at www.cpwr.com

## Slide 59: Questions?
Bruce Lippy blippy@cpwr.com
301-495-8527